## Slide 1
Milk Quality Assessment Using Spectroscopy and Machine Learning
Presented by: Md. Abu Rayhan | Department: Computer Science & Engineering | Supervisor: Md. Toukir Ahmed

## Slide 2
Why Use Spectroscopy for Milk Analysis?
Conventional Limitations
Conventional milk analysis can require laboratory testing and chemical procedures.
Rapid & Non-Destructive
Spectroscopy provides rapid and non-destructive analysis without consuming the sample.
Information-Rich Spectra
A single spectrum contains information related to multiple chemical components simultaneously.
Real-Time Monitoring
Spectroscopy can potentially support real-time or on-farm milk quality monitoring.
ML & Chemometrics
Machine learning and chemometrics are used to extract useful information from spectral data.
System Workflow
ML/Chemometric Model
Data Processing
Spectral Measurement
Milk Sample

## Slide 3
What Can Be Determined from Milk Spectra?
Parameter | Possible Application
Fat | Quantitative prediction
Protein | Quantitative prediction
Lactose | Quantitative prediction
Total Solids | Quantitative prediction
SNF | Milk composition assessment
Urea | Concentration estimation / adulteration screening
Water Adulteration | Adulteration detection
Melamine | Adulteration detection
Sucrose | Adulteration detection
Milk Powder Adulteration | Authenticity assessment
Somatic Cell Count (SCC) | Milk/udder-health related monitoring
NIR and MIR/FTIR spectroscopy are particularly useful for major milk components, while FTIR has also been investigated for adulteration detection.

## Slide 4
Spectroscopic Techniques
Near-Infrared Spectroscopy (NIR)
Commonly used for rapid milk composition analysis
Typical regions: ~700–1100 nm and 1100–2400 nm
Useful for predicting fat, protein and lactose
Mid-Infrared / FTIR
Provides strong information about molecular vibrations
Widely investigated for milk composition and adulteration
Chemometric models extract quantitative and qualitative information from FTIR spectra
Raman / Fluorescence
Also investigated for milk composition and quality assessment
Often combined with multivariate statistical models

## Slide 5
Spectral Data Preprocessing
Common Preprocessing Methods
SNV
Standard Normal Variate
MSC
Multiplicative Scatter Correction
S-G
Savitzky–Golay smoothing
1st Deriv.
First derivative
2nd Deriv.
Second derivative
Norm.
Normalization
Baseline
Baseline correction

## Slide 6
Machine Learning / Chemometric Models
For Quantitative Prediction
PLSR
Partial Least Squares Regression — particularly common in milk spectroscopy research
PCR
Principal Component Regression
SVR
Support Vector Regression
Random Forest Regression
Ensemble tree-based method
ANN
Artificial Neural Networks
For Classification
PLS-DA
Partial Least Squares Discriminant Analysis
SVM
Support Vector Machine
Random Forest
Ensemble classification
Neural Networks
Deep and shallow architectures
SVM, RF and ANN are increasingly being investigated alongside the established PLSR approach.

## Slide 7
Research Opportunity & Conclusion
Proposed Research Workflow
PLSR & ML Models
Feature Selection
Preprocessing
NIR/FTIR Spectra
Milk Samples
Possible Research Objectives
Composition Prediction
Predict fat, protein and lactose from milk spectra.
Adulteration Detection
Investigate urea/adulteration detection using spectral signatures.
Model Comparison
Compare PLSR, SVM, Random Forest and ANN.
Preprocessing Optimization
Identify the most useful spectral preprocessing method.
Assessment Framework
Develop a rapid, non-destructive milk quality assessment framework.